## Slide 1
Cyber-Power Testbed for Analyzing Distributed Control Performance during Cyber-Events
Partha S. Sarker, Niloy Patari, Brian Ha, Subir Majumder and Anurag K. Srivastava
MSCPES 2022

## Slide 2: Motivations
Typical control center-based approaches pose significant coordination and scalability challenges
Centralized control center-based architecture with single-point of failure (with backup) --> Vulnerable information and communication technologies (ICTs)
Distributed controls --> Data need not be aggregated at centralized location
Distributed techniques need to be evaluated with actual ICTs based network under realistic cyber-attacks

## Slide 3: Contributions
Testbed for emulating realistic cyber-power networks facilitating distributed optimization-based applications
Generic distributed coordination algorithm capable of identifying neighboring controllers -- facilitating inter-controller communication
Implemented realistic cyber-attacks (specifically, Man in the Middle and the Denial-of-Service attacks) within Mininet network emulator with the capability of attacking multiple hosts in the communication layer

## Slide 4: Cyber-Power Test-bed
Power System Layer : Developed with OpenDSS
Cyber Layer: Developed with Mininet
Application Layer : Developed with Python
h611
h684
h692
h675
h645
h633
h634
h652
h680
h671
h646
h632
h650
OpenDSS
Coordination Application
Distributed Optimization Application
Cyber
Attack
Application
Power System Data
Python Wrapper
Mininet
DERs Setpoint
Deployed in Mininet Hosts
Python Wrappers binds all three layers

## Slide 5: Cyber-Power Test-bed
Application Layer :
h611
h684
h692
h675
h645
h633
h634
h652
h680
h671
h646
h632
h650
OpenDSS
Coordination Application
Distributed Optimization Application
Cyber
Attack
Application
Power System Data
Python Wrapper
Mininet
DERs Setpoint
Deployed in Mininet Hosts
Node Attributes
Cyber Attacks:
  Man in the Middle
  Denial-of-Service attack

## Slide 6: Distributed Volt-Var Optimization
Volt-VAR Optimization (VVO) Problem
Primal-Dual Method for solving the problem above
independently solves OPTDIST-VC algorithm based on modified primal-dual method for VVO

## Slide 7: Test Cases & Results
Use case:
  DERs are connected at nodes 671, 684, 675, and 634.
  h634 and h671 are under attack with MitM and DoS individually.

## Slide 8: Conclusions
Developed
Testbed for cyber-power system with network emulator for distributed control application.
Distributed coordination algorithm for distributed control application.
Analyzed
Performance of distributed control during different cyber-attacks.
Findings
Distributed control is not immune to cyber-attacks.
Effects of cyber-attacks on distributed volt-var control in different nodes of the distribution system.
Advantages
Developed cyber-power test-bed can be utilized to analyze the robustness of any distributed control/optimization algorithms in the event of cyber-attacks.
Comparison between centralized and distributed controllers can be done easily in this test-bed to select the most feasible controller for a given distribution system.
Distributed controllers need to be able to identify cyber-attacks and isolate rogue nodes and self-organize.
Modeled realistic cyberattacks to test performance of distributed control application

## Slide 9
Acknowledgement to… Thank you & For Questions
Partha S. Sarker
Email: ps00030@mix.wvu.edu